## Slide 1: MIKE 11
Network Editor

## Slide 2: NETWORK EDITOR
Simulation Editor (.sim11)
Cross Section Editor (.xns11)
Parameter Editor (.HD11)
Network Editor (.nwk11)
Time Series Editor (.dfs0)
Boundary Editor (.bnd11)
Plan View, River Branches and Hydraulic Structures definition

## Slide 3: NETWORK EDITOR
Network File Displays Points, Branches, Structures and Data from Other Editors
*.NWK11 File Extension
How? MIKE Zero -> File -> New -> File -> MIKE 11 -> River Network (.nwk11)

## Slide 4: NETWORK EDITOR
Area Coordinates and Projection
How? MIKE Zero -> File -> New -> File -> MIKE 11 -> River Network (.nwk11)

## Slide 5: NETWORK EDITOR
The Graphical View displays the model branch network and background images
Graphical View

## Slide 6: NETWORK EDITOR
File Options (includes Import from ASCII)
How? MIKE Zero -> File
Import branch and point data from ASCII format
Also import from shapefile available

## Slide 7: NETWORK EDITOR
Select Items from Other Editors that will be Displayed
View Options (includes Display Settings)
How? MIKE Zero -> View

## Slide 8: NETWORK EDITOR
Automatic Tools for Repetitive Tasks
Import and Export Data to Shape File
Network Options (includes Automatic Tools)
How? MIKE Zero -> Network

## Slide 9: NETWORK EDITOR
Add Images, Shape Files and MIKE 21 Grid Files (DFS2) in the background
Change the Display Order with Overlay Manager
Add New Layer
Layer Options (Add/Remove)
How? MIKE Zero -> Layers -> Add/Remove

## Slide 10: NETWORK EDITOR
Change the Properties of Layers
Layer Options (Properties)
How? MIKE Zero -> Layers -> Properties

## Slide 11: NETWORK EDITOR
Change the View Properties of MIKE11 Objects
Settings Options (Network)
How? MIKE Zero -> Settings -> Network (Graphics)

## Slide 12: NETWORK EDITOR
Change the Mouse Settings for Digitising and Selecting Objects
Settings Options (Network)
How? MIKE Zero -> Settings -> Network (Mouse)

## Slide 13: NETWORK EDITOR
Change the Settings for Network Data
Settings Options (Network)
How? MIKE Zero -> Settings -> Network (Network Data)

## Slide 14: NETWORK EDITOR
Change the Editors that are Dynamically Linked for Editing
Settings Options (Network)
How? MIKE Zero -> Settings -> Network (Select and Edit)

## Slide 15: NETWORK EDITOR
Zoom In
Zoom Out
Previous Zoom
Next Zoom
Pan
Draw Grid
Select Objects
(cancel active tool)
Add New Points
Add New Points to Last Active Branch
Delete Points
Move Points
Define Branch (connect points)
Cut Branch into Two
Connect Branch
Disconnect Branch
Merge Branches into One
Insert Points
Exclude Points
Select order is important for some tools (eg. merge branches and insert points)
Graphical Tools

## Slide 16: NETWORK EDITOR
Inserting Objects will Open Relevant Editor
Edit Function Lists all Objects based on Zoom Scale and Cursor Sensitivity Radius
Full Right Click Functionality in Graphical View
How? MIKE Zero -> Graphical View -> Right Click (on Points and Branches)

## Slide 17: NETWORK EDITOR
The Tabular View Displays all Model Setup Data including Structures
Tabular Data is Dynamically Linked to the Graphical View
Tabular View
How? MIKE Zero -> View -> Tabular View (or short cut: Ctrl + t)

## Slide 18: NETWORK EDITOR
The Points Page Contains a List of all Digitised Points in the Model Setup
Editing in Overview
or Data Entry Panel
Chainage is
“User Defined” or
“System Defined”
based on Scaled
(Linear) Distance
Between Points
Copy/Paste
to/from Excel
for Global Editing
Points Page

## Slide 19: NETWORK EDITOR
The Branches Page
Contains Details on
Type of Branches, Direction and Model Connectivity
Branches Page

## Slide 20: NETWORK EDITOR
Topo ID
Provides a linkage to the Cross-Section
Database and allows quick change of
geometry along a Branch (ie. sections surveyed at different times)
Maximum dx
The density of computational H-points along a Branch is smaller than this value.
Link Channels
A special type of Branch that can be used to define flow between channel and floodplain
Branch Details

## Slide 21: NETWORK EDITOR
Grid point spacing in river branches (Maximum dx)
Chainage [m] : 20.000 28.000 32.000 40.000
H-point with cross section from Database
H-point with interpolated Cross Section
Q-point
Maximum dx = 5.000 m
Maximum dx = 3.000 m
Maximum dx > 8.000 m
Horizontal discretisation
Vertical discretisation

## Slide 22: NETWORK EDITOR
Setup of Channel Network
0.000
10.400
15.000
25.000
15.000
3.000
River A
0.000 - 10.400
River C
15.000 - 25.000
River B
3.000 - 15.000
Name Upstream Downstream Upstream Downstream
End End Connection Connection
River A 0.000 10.400 - River C 15.000
River B 3.000 15.000 - River C 15.000
River C 15.000 25.000 River B 15.000 -

## Slide 23: NETWORK EDITOR
The Weirs Page Contains a List of All Weirs in the Model and Options to Define Them
Plot the Position
Relative to U/S & D/S
Cross-Sections
Q/h Relations must be Calculated Prior to Runtime
Structures Page (Weirs)

## Slide 24: NETWORK EDITOR
The Culverts Page Contains a List of All Culverts in the Model and Options to Define Them
Plot the Position
Relative to U/S & D/S
Cross-Sections
Q/h Relations must be Calculated Prior to Runtime
Structures Page (Culverts)

## Slide 25: NETWORK EDITOR
The Grid Points
Page Provides a
Summary of H & Q
Points in the Model
Grid Points Page

## Slide 26: NETWORK EDITOR
The Network File can be Edited in any Text Editor
Editable Text File