## Slide 1: MIKE 11
HD Parameter Editor

## Slide 2: HD PARAMETER EDITOR
Simulation Editor (.sim11)
Cross Section Editor (.xns11)
HD Parameter Editor (.HD11)
Network Editor (.nwk11)
Time Series Editor (.dfs0)
Boundary Editor (.bnd11)
Default Values and Hydrodynamic Settings

## Slide 3: HD PARAMETER EDITOR
HD Parameter Editor Contains Initial Conditions and Resistance Data
*.HD11 File Extension
How? MIKE Zero -> File -> New -> File -> MIKE 11 -> HD Parameters (.HD11)

## Slide 4: HD PARAMETER EDITOR
Global and Local Initial Conditions
Specify Global Values in This Panel
Local Values Specified by Chainage (for Intermediate Locations Values are Linearly Interpolated)
Local Conditions
Override Global Values
Tip: Initial Conditions Should Match Water Level Boundaries at First Time Step
Initial Conditions Tab

## Slide 5: HD PARAMETER EDITOR
Global and Local Bed Resistance
Specify Global Values in This Panel
Local Values Specified by Chainage (for Intermediate Locations Values are Linearly Interpolated)
Local Conditions
Override Global Values
Lateral Resistance Factor in Cross-Section is Applied to Global or Local Values
If Lateral Resistance is Specified as a Value (not Factor), values in HD11 File are Ignored.
Bed Resistance Tab

## Slide 6: HD PARAMETER EDITOR
Bed Resistance Definition
Global and Local Variables:
Global Value
+
Local Values
(overwrites Global values at defined locations)
Resulting bed resistance
M = 30
M = 30
M = 25
M = 20
0.0 5000 10000 15000 20000 Distance [m]
Manning’s M
M = 30
M = 25
M = 20

## Slide 7: HD PARAMETER EDITOR
Different Wave Approximations Can be Solved
Specify Global Wave Approximation in This Panel
Kinematic or Diffusive Wave Can be Applied to Steep Channels with no Backwater or Tide Effects
Local Wave
Approximations Can
be Solved for Whole
or Part Branches
Wave Approximation Tab

## Slide 8: HD PARAMETER EDITOR
Default
Simulation Constants
Delta and Zeta Min
can be used to Improve Model Stability
Default Values Tab

## Slide 9: HD PARAMETER EDITOR
Mark the check
boxes to save additional information to the result file
Separate File is Created with “HDAdd” added to the Name Specified in the Simulation Editor
Additional Output Tab

## Slide 10: HD PARAMETER EDITOR
Maps Tab - Flood Mapping from 1-D Model

## Slide 11: HD PARAMETER EDITOR
Maps Tab – for 1D FLOOD MAPPING
How? HD Parameter File -> Maps Tab
Uses Linear Interpolation between Cross-Sections
Map Position, Extent and Resolution are User Defined
Static or Dynamic Data (All or Part of Simulation Length)
Different Items can be Mapped eg. Level, Depth, Invert (DEM)
Advanced Maps can be made if 2-D Ground Data is Available

## Slide 12: HD PARAMETER EDITOR
1-D FLOOD MAPPING
Grid File Definition (DFS2 File Type)
K
J
DFS2 Grid File

## Slide 13: HD PARAMETER EDITOR
1-D FLOOD MAPPING
Type and Items to Map
Item:
Water level
Water depth
Velocity
Velocity * Depth
AD component
DEM
h,p,q
Type:
Static (Max/Min)
Dynamic
Component only used for AD

## Slide 14: HD PARAMETER EDITOR
1-D FLOOD MAPPING
Temporal Settings (Dynamic Items Only)
Multiple of the Time Step in MIKE11
Full Period of Simulation
Start and End Times for Part Simulation

## Slide 15: HD PARAMETER EDITOR
1-D FLOOD MAPPING
DEM Input Data Options
Use 2-D Data to Refine Mapping

## Slide 16: HD PARAMETER EDITOR
DEM Output Options
DEM type can be used to make a grid of the channel geometry:
Channel only (Recommended)
Inserted directly into larger floodplain grid (improve DEM by burning river channel into the original DEM)
Best results achieved for: - small dX
- Cross-section extents defined using coordinates

## Slide 17: HD PARAMETER EDITOR
ArcGIS
Also:
Plot Composer
Result Viewer
MIKE Animator
Grid Editor
Visualising Mapping Results (*.dfs2)

## Slide 18: HD PARAMETER EDITOR
The HD Parameter File can be Edited in any Text Editor
Editable Text File