## Slide 1: MIKE 11
Calibrating the NAM model

## Slide 2: Initial Conditions
Data to be specified:
Initial Water Content of Surface and Root zone storages
Initial values for Overland flow and Interflow
Initial Groundwater Depth ~ Initial baseflow
Recommended to disregard the first half year or so of the results to eliminate erroneous Initial Conditions!

## Slide 3: NAM Model Calibration
Most NAM parameters of empirical nature => values must be determined by calibration:
Water balance in system
Runoff hydrographs, peak and shape
Comparison of runoff results with observations
Generally recommended to change only one parameter between each run - to discern the effect !

## Slide 4: NAM Model Calibration
A. Manual step-by-step procedure (changing one variable at a time)
Autocalibration Automatic optimisation routine using multi-objective optimisation strategy
4 objectives available: 1) Overall volume error (= water balance) 2) Overall root mean square error (= hydrograph shape) 3) Root mean square error of peak flow events 4) Root mean square error of low flow events
Easy to use - BUT EVALUATION OF VARIABLE VALUES
REQUIRED TO JUDGE HYDROLOGICAL SENSITIVITY

## Slide 5: NAM Model Calibration
CALIBRATION OF NAM
Subjective fitting of observed stream flow hydrographs by
TRIAL AND ERROR

UNDERSTAND PARAMETERS

## Slide 6: NAM Model Calibration
Maximum 15 NAM parameters :
5 parameters usually fixed
10 parameters to be calibrated
3 parameters (Lmax, Umax, CQOF) most important for the water balance
Remaining parameters for minor adjustments and for routing

## Slide 7: NAM Model Calibration
Umax : Maximum water content in surface storage
Effects mainly:
    Overland flow/infiltration
    Evapotranspiration
    Interflow
Consequence of increasing Umax:
    Less overland flow (especially in start of wet periods)
    Higher evapotranspiration
    Reduced infiltration
    Higher interflow
Guidelines: Umax ~ 0.1 * Lmax => Umax ~ 10-20 mm

## Slide 8: NAM Model Calibration
Lmax : Maximum water content in lower zone / root zone storage
Effects mainly:
Overland flow/infiltration
Evapotranspiration
Baseflow
Consequence of increasing Lmax:
Higher evapotranspiration
Reduced overland flow
Higher infiltration
Reduced baseflow

## Slide 9: NAM Model Calibration
CQOF: Overland flow coefficient (Value range: 0-1)
Determines amount of overland flow and infiltration
Flat, highly permeable soils : CQOF ~ 0:
  Little overland flow
  High infiltration
Steep, impermeable soils, rocks : CQOF ~ 1:
  Large overland flow
  Small infiltration

## Slide 10: NAM Model Calibration
CKIF : Interflow drainage coefficient
= Time constant for drainage of surface storage as “interflow”
Consequence of increasing CKIF:
  Linear amplification of interflow
  Reduced infiltration
  Reduced overland flow
CKIF = 500-1000 hours

## Slide 11: NAM Model Calibration
TOF overland flow
TIF threshold values for interflow
TG groundwater recharge
values between [0 -1]
No flow is generated if the relative soil moisture content L/Lmax < threshold value

## Slide 12: NAM Model Calibration
Consequence of increasing TOF:
Later start of overland flow in beginning of wet season
Higher infiltration
Consequence of increasing TIF:
Later start of interflow in beginning of wet season
Higher infiltration and overland flow
Consequence of increasing TG:
Later start of groundwater recharge and flow in beginning of wet season
Quicker filling of root zone
Threshold values reflect degree of spatial variability

## Slide 13: NAM Model Calibration
CK1, CK2 and CKBF time constants for linear reservoir routing
CK1 and CK2 for routing overland flow and interflow along catchment slopes and through channels down to outlet of catchment.
  Usually set CK1 = CK2
CKBF for routing recharge through linear g.w. storage.
  Usually CKBF >> CK1/CK2
Consequence of increasing CK:
  Longer duration of flow
  Lower peaks

## Slide 14: NAM Model Calibration
Note: The actual values of CK has no effect on generated
flow volumes seen over long time, but only on the
shape of the hydrographs

## Slide 15: NAM Model Calibration
Calibration strategy
Fit of water balance of calibration period Adjust actual evapotranspiration by adjusting Lmax/Umax
Fit of flood peaks Adjust overland flow - Volume : CQOF - Magnitude - Timing : TOF - Shape : CK1 = CK2
Fit of low flows Adjust baseflow - Volume : adjust overland flow adjusted recharge i.e. again CQOF - Timing : TG - Shape : CKBF
Verify on different data e.g. split-sample test

## Slide 16: NAM Model Calibration
NAM simulation, Liver creek

## Slide 17: NAM Model Automatic Calibration
NAM automatic calibration
Basic NAM model (9 parameters)
Multiple objectives optimised simultaneously
  Water balance
  Overall hydrograph shape
  Peak flows
  Low flows
Preferably use two optimisation objectives
  Water balance
  One RMSE objective, according to the purpose of the model

## Slide 18: NAM Model Automatic Calibration
NAM automatic calibration
Global optimisation routine: Shuffled Complex Evolution (SCE) algorithm
Efficiency: about 2000 model evaluations (typically 1-2 CPU minutes)
Number of iterations may be increased if needed
The optimisation process will stop in case convergence is obtained before the last iteration

## Slide 19: NAM Model Automatic Calibration
NAM automatic calibration
Results for the first months of the simulation depend on initial conditions and may be inaccurate
It is hence recommended to:
  Manually adjust initial conditions to best fit the observed data
  Exclude the first months from the optimization evaluation

## Slide 20: NAM Model Automatic Calibration
NAM automatic calibration
After auto-calibration, check the calibration plot :

## Slide 21: NAM Model Automatic Calibration
NAM automatic calibration
Also check *_Autocal.txt file : contains calculated parameters for each iteration

## Slide 22: NAM Model Automatic Calibration
NAM automatic calibration
Also check RRStat.txt file : contains annual summaries

## Slide 23: NAM Model Automatic Calibration
NAM automatic calibration
Remarks:
All NAM calibrated parameters are updated at the end of the auto-calibration process
You hence need to close and re-open the file to work with new parameters’ values