## Slide 1: MIKE 11
Rainfall Runoff using the FEH Method

## Slide 2: Modelling Rainfall-Runoff using FEH

## Slide 3: The FEH Model
Standard Rainfall Runoff method in the UK
FEH (Flood Estimation Handbook) was introduced in 1999 to replace previous Flood Studies Report (FSR) methods for flood estimation in the UK
FEH constitutes an alternative to the continuous models such as NAM for flood simulation

## Slide 4: The FEH Model
FEH is a unit hydrograph method
Linear response to rainfall
Event-based

## Slide 5: The FEH Model
Loss
Net rainfall
The FEH models divide the storm rainfall in excess/net rainfall (or runoff) and water loss (or infiltration)

## Slide 6: The FEH Model
Flood Estimation Handbook
Overview:
Five volumes
  Overview
  Rainfall Frequency Estimation
  Statistical Procedures for Flood Frequency estimation
  The Flood Studies Report (FSR) rainfall-runoff method
  Catchment Descriptors
Two CDs
  FEH CD-ROM: Digital descriptors for all catchments in the UK
  WINFAP-FEH: Statistical analysis to arrive at a T-year flood
MIKE 11
FEH main focus

## Slide 7: The FEH Model
The MIKE 11 FEH module generates flood hydrographs based on catchment descriptors extracted from the FEH CD-ROM
Three main methods are available for hydrograph generation:
Generation of a T-year event
Generation of a Probable Maximum Flood (PMF)
Generation of an observed Flood Event

## Slide 8: The FEH Model
The three methods differ mainly in the rainfall inputs which are respectively:
Statistically derived to produce a T-year event
Probable Maximum Precipitation (PMP)
Actual Rainfall

## Slide 9: The FEH Model
Regardless of the type of hydrograph method the response is governed by three main parameters:
Time to peak: Timing and shape
Percentage runoff: Loss estimation
Baseflow: Background groundwater runoff

## Slide 10: FEH Unit Hydrograph
Hydrograph (distribution of the runoff in time): (Unit Hydrograph: Unit pulse response function of linear hydrological system) FSR triangular hydrograph: (The standard hydrograph)
time
Up=2.2/Tp
TB=2.52Tp
(m/s/mm)
Time to peak: Tp

## Slide 11: Determining the Time to Peak Tp
Tp(0) time to peak of Instantaneous Unit Hydrograph (IUH)
Tp(DT) time to peak of DT-Unit Hydrograph (SUH)

## Slide 12: Determining the Time to Peak Tp
Tp(0) can be determined through 4 different methods:
From observed flood event data
  Analysis carried out outside MIKE 11
From catchment lag
From catchment descriptors
  A regression on 4 of the catchment descriptors is carried out
From a donor catchment
  Use observed data from a similar catchment to adjust time to peak found through the catchment descriptor method

## Slide 13: Time to peak Tp from Catchment Lag
Time to peak determined by
p
Q
t
t
LAG

## Slide 14: Time to peak Tp from catchment Descriptors
A regression on 4 of the catchment descriptors is used
Where:
DPSBAR: Mean drainage path slope (m/km)
PROPWET: Proportion of time when Soil Moisture Deficit (SMD) was below 6 mm during the period 1961-90
DPLBAR: Mean drainage path length (km)
URBEXT: Extent of urban and sub-urban land cover

## Slide 15: Time to peak Tp from Donor Catchment
Method:
Apply catchment descriptor method at un-gauged site
Apply catchment descriptor method at gauged site
Estimate the time to peak at gauged site based on observed data
The time to peak from the subject site is then adjusted according to:

## Slide 16: Determining the Percentage Runoff (PR)
The percentage of the total rainfall input which becomes direct response runoff in the river.
With the rural Percentage Runoff PRRURAL given by:
SPR is the Standard Percentage Runoff.
DPRCWI is dependent on the catchment wetness index CWI (function of SAAR):
DPRRain is dependent on the rain intensity:

## Slide 17: Catchment Wetness Index (CWI)
Figure 3.7 i FEH Vol. 4

## Slide 18: Determining the standard Percentage Runoff Fraction(SPRF)
SPRF can be determined through 4 different methods:
From observed flood event data
  Analysis carried out outside MIKE 11
From Baseflow index
From catchment descriptors
  A regression on the hydrology of Soil Types (HOST) is carried out
From a donor catchment
  Use observed data from a similar catchment to SPR found through the catchment descriptor method

## Slide 19: SPRF from Baseflow Index (BFI)
SPR determined by
BFI varies between 0.1 and 0.99 - corresponding to the degree of impermeability

## Slide 20: SPRF from Catchment Descriptors
SPR determined by
SPRi varies between 2% and 60% - and is given as one of the catchment descriptors

## Slide 21: SPR from Donor Catchment
Method:
Apply catchment descriptor method at un-gauged site
Apply catchment descriptor method at gauged site
Estimate SPR at gauged site based on observed data
The standard percentage runoff from the subject site is then adjusted according to:

## Slide 22: Determining the Base Flow (BF)
The flow in the river prior to the storm event
Parameter less important than Time to peak and SPR
Q
t
BF

## Slide 23: Determining the Base Flow(BF)
BF can be determined through 3 different methods
From observed flood event data
  Analysis carried out outside MIKE 11
From catchment descriptors
  A regression analysis is carried out
From a donor catchment
  Use observed data from a similar catchment to adjust time to peak found through the catchment descriptor method

## Slide 24: Base Flow from Catchment Descriptors
A regression on catchment descriptors is used
Where
CWI: Catchment Wetness Index (function of SAAR)
SAAR: Standard Average Annual Rainfall (1961-90) (mm)
AREA: Catchment Area (km2)

## Slide 25: BF from Donor Catchment
Method:
Apply catchment descriptor method at un-gauged site
Apply catchment descriptor method at gauged site
Estimate BF at gauged site based on observed data
The Baseflow from the subject site is then adjusted according to

## Slide 26: The FEH hydrograph
Based on the three main parameters the hydrograph is found through
The net event hyetograph is found by multiplying the design hyetograph by PR
By the method of convolution the rapid response hydrograph is found
The Base flow is added to produce the final response