## Slide 1: MIKE 11
Cross Section Editor

## Slide 2: CROSS SECTION EDITOR
Simulation Editor (.sim11)
Cross Section Editor (.xns11)
Parameter Editor (.HD11)
Network Editor (.nwk11)
Time Series Editor (.dfs0)
Boundary Editor (.bnd11)
Editor and Database of Cross-Sections

## Slide 3: CROSS SECTION EDITOR
Raw Data View
Processed Data View
(calculated from Raw Data
and used in Simulation)
Database Definition
The Database File:
  Is Binary (cannot be viewed in a Text Editor)
  Can hold many Cross-Sections, each identified by:
    River Name (Branch)
    Topographical Identifier (Topo ID)
    Chainage (increasing in downstream direction)
A Single Cross-Section Includes:
  Information on Section and Radius Type
  Raw Data (X,Z-values defining the bed level)
  Information of Lateral Roughness Formulation
  Markers defining extent of the Cross-Section
  Processed Data tables including
    Hydraulic Radius
    Area and Storage Width
    Conveyance

## Slide 4: CROSS SECTION EDITOR
Cross-Section Editor
Displays Raw and
Processed Data
*.XNS11 File Extension
How? MIKE Zero -> File -> New -> File -> MIKE 11 -> Cross Sections (.xns11)

## Slide 5: CROSS SECTION EDITOR
Import Raw and Processed Data
From ASCII
File Options (includes Import and Export)
How? MIKE Zero -> File

## Slide 6: CROSS SECTION EDITOR
1. Properties
2. Tree
3. Tabular
4. Functions
5. Graphical
1
2
3
4
5
Raw Data View (Five Editing Panels)

## Slide 7: CROSS SECTION EDITOR
Full Right Click
Functionality at Each Tree Level
Raw Data View (Tree Panel)

## Slide 8: CROSS SECTION EDITOR
Rename Branches
and Cross-Sections
Branch Level
Section Level
Tree Panel (Right Click Rename)

## Slide 9: CROSS SECTION EDITOR
Branch Level
Section Level
Copy Branches
and Cross-Sections
Tree Panel (Right Click Copy)

## Slide 10: CROSS SECTION EDITOR
Interpolate Single or Multiple Cross-Sections
Tree Panel (Right Click Insert Interpolated)

## Slide 11: CROSS SECTION EDITOR
Edit Options (Applies to Tabulated Data Panel)
How? MIKE Zero -> Edit

## Slide 12: CROSS SECTION EDITOR
Five Commonly Used Bank Markers
Bank Markers Affect the
Calculation of Processed Data
Bank Markers are Displayed
in Graphical View
Tabulated Data Panel (Bank Markers)

## Slide 13: CROSS SECTION EDITOR
Raw Data View (Graphical Panel)
Plot of Section (looking D/S)
Bank Markers 1 & 3:
Determines Effective Area of cross section to be included in simulation
Effective flow area

## Slide 14: CROSS SECTION EDITOR
Plot of Section (looking D/S)
Bank Markers:
Displayed as Red Lines
Can be Assigned Directly in Graphical View
Lateral Resistance:
Displayed as Blue Line
Units on Right Axis
Bed Level:
Left Axis Denotes Level
Each Row in Table Assigned a Point in Graph
Cross-Section History Displayed as Grey Shadow
Raw Data View (Graphical Panel)

## Slide 15: CROSS SECTION EDITOR
Clear Grey Shadow
Cross-Section History
Graphical Panel (Right Click Menu and Tools)

## Slide 16: CROSS SECTION EDITOR
Raw Data View (Properties Panel)

## Slide 17: CROSS SECTION EDITOR
Section Type: Open / Closed (Irregular, Circular, Rectangular)
Cross section ID: User defined text identifier
Datum: Reference level (m)
Radius Type: Resistance or Hydraulic Radius (Total or Effective Area)
Coordinates: Manual Override of Default Display of Extents
Resistance:
Transversal Distribution - Uniform, High/Low flow zones, Distributed
Resistance Type - Relative Resistance (multiplier of section value)
- Manning’s n and M
- Chezy Number, Darcy-Weisbach (k)
Properties Panel (Summary)

## Slide 18: CROSS SECTION EDITOR
Different formulation due to different assumptions about
the Bed Shear Stress distribution across the river bed
Resistance Radius:
Resistance radius formulation is used.
Hydraulic Radius: - Total Area uses raw section geometry - Effective Area includes adjustment based on relative resistance variation
Radius Type (Resistance versus Hydraulic)
o
o

## Slide 19: CROSS SECTION EDITOR
Resistance Radius:
Hydraulic Radius:
Radius Type (Resistance versus Hydraulic)
y
A
B
P
Smoother transition from deep to shallow in processed data tables
Includes more accurate side wall effects in deep narrow channels

## Slide 20: CROSS SECTION EDITOR
Bed Resistance
Formulations:
  Manning-Strickler M [m1/3 /s]
  Manning’s coefficient n(= 1/M) [s/ m1/3]
  Chezy’s coefficient C [m1/2 /s]
Relative resistance:
Resistance Number = Resistance factor * Bed Resistance number
(Cross section database) (HD Parameter file) (default: = 1.0) (default: M = 30)

## Slide 21: CROSS SECTION EDITOR
Flood plain
n=0.075;
Channel
n=0.025
Flood plain
n=0.075
X
Z
Resistance definition Absolute Resistance:

## Slide 22: CROSS SECTION EDITOR
Resistance definition Relative Resistance:
Flood plain
n=0.075, r=3
Channel
n=0.025, r=1
Flood plain
n=0.075, r=3
X
Z

## Slide 23: CROSS SECTION EDITOR
Dynamic Links to Processed Data
Opens Processed Data View
Updates Markers in Selected Cross-Section:
(1) Furthest Left Extent
(2) Lowest Point
(3) Furthest Right Extent
Functions Panel

## Slide 24: CROSS SECTION EDITOR
Processed Data View includes:
Tree View listing of all Cross-Sections
Tabular Data of all hydraulic parameters
Graphical View of the selected parameter
For Each Section:
Area, Hydraulic Radius, Storage Width & Conveyance calculated for different water levels
Additional Storage Area (optional)
Resistance Factor (optional)
User can Control the Density of Processed Data Points
Processed Data View (Definition)

## Slide 25: CROSS SECTION EDITOR
Similar Layout and Functionality as the Raw Data View
Graphical View is Right Click Enabled
Select Item to Plot
Processed Data View (Overview)
How? ”View Processed Data” Button in Raw Data View

## Slide 26: CROSS SECTION EDITOR
Protects Manually Changed/Added Data from Automatic Update
Switch Back to Raw Data
Options for Density and Distribution of Processed Data Points:
Automatic
Equidistant
User Defined
Recompute All
Processed Data View (Functions)

## Slide 27: CROSS SECTION EDITOR
Apply Global Changes to Raw and Processed Cross-Section Data
Cross-Section Options (including Global Edit)
How? MIKE Zero -> Cross-Sections -> Apply to All Sections
NOTE
Great for ensuring, that all cross sections have been precalculated prior to initiating the simulation

## Slide 28: CROSS SECTION EDITOR
Change the Appearance of Objects in the Graphical View
Setting Options (Graphics)
How? MIKE Zero -> Settings -> Cross-Section

## Slide 29: CROSS SECTION EDITOR
Change the Drawing Options for the Graphical View
Setting Options (Drawing)
How? MIKE Zero -> Settings -> Cross-Section

## Slide 30: CROSS SECTION EDITOR
Miscellaneous Settings including Default Values
Setting Options (Miscellaneous)
How? MIKE Zero -> Settings -> Cross-Section

## Slide 31: CROSS SECTION EDITOR
Change Markers that are Automatically Updated
Setting Options (Update Markers)
How? MIKE Zero -> Settings -> Cross-Section